## Slide 1: Using a TIMES approach to assess low-carbon transport and climate change mitigation policy scenarios
November 2019
Olivier Bahn olivier.bahn@gerad.ca
Kathleen Vaillancourt kathleen@esmia.ca

## Slide 2: Simplified classification of E3 models

## Slide 3: Simplified classification of E3 models
Top-down
Hybrid
Bottom-up
Typically used for:
Evolution of energy systems, emerging technologies, GHG mitigation costs
Less energy details
Full economy
Macro economic
More energy details
Partial economy
Techno-economic
Typically used for:
Macroeconomic impacts (jobs, GDP, etc.) of energy and climate policies

## Slide 4: Simplified classification of E3 models
Top-down
Hybrid
Bottom-up
Examples:
Optimisation models
Simulation models
Less energy details
Full economy
Macro economic
More energy details
Partial economy
Techno-economic
Examples:
General equilibrium models
Econometric models

## Slide 5: Simplified classification of E3 models
Simulation
Optimisation
Exploratory models to assess the impacts of changes on energy systems
Previsions
Business-as-usual scenarios
Most likely outcomes
Models that focus on specific criteria (e.g. costs) to assess changes in energy systems
Projections
Energy transition scenarios
Ideal outcomes

## Slide 6: The TIMES model generator

## Slide 7: ETSAP – International Energy Agency
Developed within the Energy Technology Systems Analysis Programme (ETSAP) of the International Energy Agency (IEA) since 1978
With the purpose of coming up with a common (optimisation) platform for countries to examine the evolution of their energy systems in response to technology developments and policy priorities
Since then, concerns over economic sustainability, climate change, energy security, and social safety call for an energy revolution with increasing urgency and a joint international effort is even more necessary than forty years ago
Long and rich history of methodological developments and applications to support decision making in nearly 70 countries
Canadian researchers at GERAD are among the prime developers

## Slide 8: Reference Energy System (RES)
TIMES is based upon the concept of the Reference Energy System (RES)—or energy network—that represent all possible flows of energy within the integrated energy sector

## Slide 9: TIMES Characteristics
TIMES combines advanced versions of MARKAL models
Integrated energy systems: capture the whole energy system (multi-fuel, multi-sector, multi-region)
Demand driven: Useful demands correspond to energy services demands may be elastic to their own prices
Dynamic model: over 30 to 50 years to capture long term structural changes (or even 100 years for climate policies)
Simulates market competitions (of energy carriers and technologies) through an optimisation (LP)
Computes a partial equilibrium
→ minimize the total discounted cost (or equivalently, maximise the net social surplus)

## Slide 10: Space and time dimensions
Space
Uni- or multiregional models
Geographical scales:
  Global
  Continental
  Multinational
  National
  Regional (Provinces, States, etc.)
  Cities
Time
Base year
Annual time periods
Milestone years (results)
Annual data (flexibility)
Time slices (seasons and intraday periods)

## Slide 11: In summary ….
TIMES
Technology investments and annual activities
Emission trajectories
Adjusted demands for energy services
Marginal prices of energy forms
Imports/exports of energy and emission permits
Total discounted system cost
Equilibrium
Policies
GHG caps
Taxes, subsidies
Sectors’ measures
Energy service demands
Demand price-elasticities
Price of imported/exported commodities
Reserve supply curves
Discount rate
Economic – Energy Inputs
Techno-economic database
Technical
Inputs and outputs
Availability factors
Efficiencies
Lifetime
Installed capacity
Emission coefficients
Economic
Investment costs
Fix operation costs
Variable operation costs
Hurdle rates
Market shares

## Slide 12: The NATEM model North American TIMES Energy Model

## Slide 13: NATEM
TIMES optimization model
Demand driven – energy services
Price-elasticities of demands
Dynamic model over 40 years
Simulates market competitions
Computes a partial equilibrium
→ minimise the total cost discounted at 3-4%
→ compute the marginal reduction cost
Canada – 13 regions
Horizon 2011-2050
9 periods, 16 time slices for electricity

## Slide 15
Small cars, short distance
Large cars
Light trucks
Light trucks
Medium trucks
Heavy trucks
Urban buses
Intercity buses
School buses
Motos
Off road
Trains
Trains
Airplanes
Airplanes
Ships
Gasoline
Diesel
Propane
CNG
Electricity
Ethanol
Biodiesel
Methanol
FT diesel
Jet fuel
Fuel oil
Hydrogen
Passenger
transportation
Vehicle category
Pkm
Pkm
Pkm
Pkm
Pkm
Pkm
Pkm
Pkm
Pkm
Pkm
Freight
transportation
Vehicle category
Vehicle Type
(ex. small cars)
Tkm
Tkm
Tkm
Tkm
Tkm
Tkm
Fuels
Small cars, long distance
Pkm
ICE, Improved, GSL
ICE, Hybrid, GSL
ICE, Standard, GSL
PHEV20 Lithium-ion
BEV150 Lithium-ion
Natural gas
Propane
Flex fuel
ICE, Standard, DST
ICE, Improved, DST
ICE, Hybrid, DST
PHEV50 Lithium-ion
BEV300 Lithium-ion
Cellulosic E
Butanol
LNG
Biojet
Charging station, Residential
Charging station, Public

## Slide 16: Scenario analysis approach

## Slide 17
http://iet.polymtl.ca/tefp

## Slide 19
https://www.springer.com/gp/book/9783319744230

## Slide 20
iet.polymtl.ca/energy-outlook
The only Outlook including deep decarbonisation scenarios in Canada.
Results at the provincial level.
Reduction scenarios up to -80% by 2050 from 1990 levels.
This goal, like the intermediate GHG targets, will be missed by a lot unless there is a significant turnaround.

## Slide 21: Scenarios for GHG mitigation
BAU : Existing policies
PRO : Individual provincial targets
FED : Federal targets (30% by 2030 and 80% by 2050, from 2005 levels)
  All reductions must be achieved domestically.
FIM : Federal targets with 25% international carbon market purchases
80P : Deeper target (80% by 2050, from 1990 levels)

## Slide 22: GHG emissions by sector

## Slide 23: Final energy consumption - transportation

## Slide 24: Market shares of light-duty vehicles

## Slide 25: Marginal reduction cost

## Slide 26: All results available by province - Quebec

## Slide 27: Thank you for your attention!
July 2019
November 2019

## Slide 28: EXTRA SLIDES

## Slide 29: For the Ministry of Environment of Quebec (MELCC)
http://www.environnement.gouv.qc.ca/changementsclimatiques/trajectoires-emissions-ges.pdf

## Slide 30: Marginal abatement cost curves for 2030

## Slide 31: For the Metropolitan Montreal Community
Montreal wants to be a leader in climate action, by achieving carbon neutrality in 2050.
Collaboration to develop a GHG reduction plan, an adaptation / resiliency plan and define new GHG reduction measures in consultation with key stakeholders.
Modeling is necessary to establish GHG reduction trajectories that allow to achieve the objectives of five metropolitan zones in 2030 and 2050.
Development of a multiregional urban TIMES model for the five zones of the Metropolitan Montreal Community (MMC).

## Slide 32: Technology mixes at a finer special resolution
Chart: Draft results: LDV in the city of Montreal
| REF | GES1 | GES2 | GES3 | GES4 | REF | GES1 | GES2 | GES3 | GES4 | 2015 |  | 2030 |  | 2050
ICE | 566.0813 | 198.4458 | 96.6967 | 96.6967 | 94.0042 | 0 | 370.3389 | 0 | 0 | 0 | 0
Hybrid | 80.6478 | 230.7656 | 254.944 | 283.7942 | 330.82 | 0 | 137.0437 | 503.5221 | 413.6082 | 187.2707 | 0
Plug-in hybrid | 0.24886 | 28.5409 | 28.5409 | 28.5409 | 28.5409 | 0 | 0 | 0 | 0 | 0 | 0
Electric | 0.24886 | 179.6816 | 179.6816 | 179.6816 | 179.6816 | 0 | 255.4283 | 309.259 | 399.1728 | 625.5104 | 0
Flex Fuel | 0 | 54.8608 | 132.4315 | 103.5813 | 59.248 | 0 | 0 | 0 | 0 | 0 | 0
Natural gas | 0.28238 | 26.0453 | 26.0453 | 26.0453 | 26.0453 | 0 | 49.9702 | 0 | 0 | 0 | 0
Propane | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: Draft results: Heating systems in commercial buildings of the City of Montreal
| REF | GES1 | GES2 | GES3 | GES4 | REF | GES1 | GES2 | GES3 | GES4 | 2015 |  | 2030 |  | 2050
Electric systems | 0.73461 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 7.6937 | 9.4485 | 0
Heatpumps - Electricity | 1.4041 | 5.7207 | 6.3024 | 10.0588 | 10.0588 | 0 | 6.6584 | 14.3826 | 14.1958 | 14.1958 | 0
Heatpumps - Natural gas | 0.13689 | 0.38425 | 0.38809 | 0.38809 | 3.4607 | 0 | 0.44517 | 7.7228 | 2.3134 | 0.55856 | 0
Central heat systems | 0.010238 | 0.0067653 | 0.0065623 | 0.0064947 | 0.0064947 | 0 | 0.00033993 | 0.00032634 | 0.00032294 | 0.00032294 | 0
Heating oil systems | 1.6483 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Natural gas systems | 17.5703 | 16.1829 | 14.8506 | 10.8452 | 7.7726 | 0 | 18.5601 | 2.3896 | 0 | 0 | 0
LPG systems | 0.52397 | 0.34625 | 0.33586 | 0.3324 | 0.3324 | 0 | 0.017398 | 0.016702 | 0.016528 | 0.016528 | 0
Geothermal systems | 0.0022253 | 0.012267 | 0.011899 | 0.011777 | 0.011777 | 0 | 0.029261 | 0.02809 | 0.027797 | 0.027797 | 0
Solar systems | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0